## Slide 1: ISNE 101
Week 3
Dr. Ken Cosh

## Slide 2: Recap
Last week we talked about binary.
And hence encoding things into a binary form - digitisation!
Remember Huffman?
This Week
Communication and Networks

## Slide 3: The Evolution of Communication

## Slide 4: Earliest Communication

## Slide 5: Speech
Sets Humans apart from animals
Estimated 1.5million-200,000 years ago
Mutation of the FOXP2 gene
Facilitated transfer of knowledge through generations
Forms the basis of written languages.

## Slide 6: Progress towards Writing
Symbols
Allow message longevity but represent speech acts
Cave Paintings
Oldest date from around 30,000 BC
Petroglyphs
Around 10,000 BC carving developed to make incisions
into rock surface
Pictograms
While Petroglyphs show a single scene, Pictograms
narate a story
Ideogram
Ideograms represent concepts such as emotions

## Slide 7: Writing
Around 2-3,000 BC the Sumerians developed the first writing system.
Evolved from Pictograms
Developed into Cuneiform
Around 1,000 characters -> 400 characters (Hittite
Cuneiform)
Symbols pressed into clay
Egyptian Hieroglyphs were derived from Sumerian writing.
"It is a complex system, writing figurative, symbolic, and phonetic all at once, in the same text, the same phrase, I would almost say in the same word." (Champollion)

## Slide 8: Developing an Alphabet
Egyptian Hieroglyphics were logosyllabic, i.e. symbols stand for;
Words
Sounds
or to place a word in a category
The Phonetic components of Hieroglyphs were crucial to developing an alphabet.
The Egyptians developed a set of 22-24 Hieroglyphs which were used to record foreign names etc.

## Slide 9: Proto-Sinaitic
Also known as Proto-Canaanite
Around 2,000-1,700 BC
Migrant workers translated Egyptian Hieroglyphs into the Canaanite language
E.g. The Egyptian "Pr" (or Per), meant house
(or Floorplan). This became "bayt", which
was Canaanite for house.
Acrophony is when a letters name begins with the letter itself.
Bayt ---> "Bet" ---> "Beta" ---> "B"

## Slide 10: Spreading the Word

## Slide 11: The Greeks
Vowels were a hindrance when writing in Pheonician, (as well as Egyptian / Hebrew).
But in Greek they were essential, and afforded equal status as consonants.
Together with the "Latins" (Romans) the alphabet evolved into this!
Other tribes evolved their alphabets differently, but most stem from the Proto-Sinaitic.

## Slide 12: Communication Technology?
What technology have we discussed so far?

## Slide 13: The Printing Press
105AD - Chinese invent paper
The Chinese also developed wood-block printing, and books with hard covers and movable type (circa. 1041).
However, Chinese has thousands of characters, so traditional block printing was still preferred.
~1440 - Gutenburg 'invented' the printing press
Ability to mass print books.
Whereas before it could take a monk 20 years to transcribe the bible
Gutenburg combined a variety of mechanical technologies
to perfect his invention.

## Slide 14: The Printing Press
Gutenburg was named #1 person of the millennium by A&E Network & Time Life.
Ahead of;
Christopher Columbus Freud
Galileo Galilei Einstein
Shakespeare Lincoln
Newton Darwin
Da Vinci Beethoven
Why did this technology invention have such a great impact?

## Slide 15: Telecommunication
Transmission of signals over a distance, for the purpose of communication.
Visual, Audio (and later electronic)
Fires
Beacons
Smoke Signals
Drums
Horns

## Slide 16: Telecommunication
The Problem:
How do we use fires / beacons / smoke signals to send a message;
Consider the fire beacons in Lord of the Rings.
N0 FIRE = No Problem
FIRE = Problem!
The Solution:
Semaphore

## Slide 17: Hydraulic Telegraph
Circa 400BC

## Slide 18: Semaphore
France 1792.
2*2m long arms with 7 positions
1*cross bar with 4 angles
7*7*4 = 196
196 different symbols
556 stations following line of sight
Total distance 4,800km
Paris to Lille = 15 stations / ~32 mins

## Slide 19: Semaphore
Sweden -->
UK
Germany -->

## Slide 20: Electrical Telegraph
The presence and flow of charge
Electrons & Protons
Very Fast
Early versions used a grid like this->
Later Morse invented his code.
This pre-dates Optical Semaphore

## Slide 21: Electrical Telegraph
Requires 'wires', which is a problem particularly at wartime.
Maxwell: "We have strong reason to conclude that light itself is an electromagnetic disturbance in the form of waves propagated through the electromagnetic field."
Marconi demonstrated that communication is possible wirelessly

## Slide 22: Telephone, Television...
1876: Bell demonstrated the telephone
Now the wires can talk.
Combine this with Marconi, and the airwaves start to sing - we have radio.
Add some pictures & we have a TV.

## Slide 23: Telecommunication Systems
Comprised of Hardware and Software arranged to transmit data from one location to another.
  Establish interface between sender and receiver
  Routes messages (packets) along most efficient paths
  Basic information processing to make sure the right message gets to the right receiver
  Basic editorial tasks, rearranging format, checking for transmission errors
  Converts message speeds (from slower cable to speed of computer).
  Controls flow of information through a network.

## Slide 24: Packet Transfer
To improve the efficiency of a network, data streams are broken into packets.
Packets are smaller bundles of data.
Packets are different sizes dependent on the protocol or standard being used – the X.25 packet switching standard uses packets sized 128bytes.

## Slide 25: Packet Switching

## Slide 26: Protocols
With telecommunications systems using a wide variety of diverse devices, a common set of rules are needed to enable them to ‘talk’ to each other.
The set of rules is called a Protocol.
  TCP/IP
  FTP
  WAP
  HTTP
Each device identifies the receivers protocol so they can send data in the right way, and to check it arrived without problem.

## Slide 27: Layered Protocols
TCP/IP consists of many protocols, which are divided into layers;
Application Layer
Includes things like Bittorrent, DNS...
Transport Layer
Primarily tasked with forming data packets, adding
header information etc.
Internet Layer
Includes IP, functions such as addressing / routing
Link Layer
Deals with actual data exchange, error checking, Bit
Rate etc.

## Slide 28: Internet Protocol
Every PC / Printer etc. has a unique IP address.
  IP addresses represent a 32 bit word
But, this is translated to ‘decimal-dot’ notation to make life easier! – More like a phone number.
  172.17.28.143
  Each number is between 0 and 255 (i.e. an 8 bit number in binary)
Totally 256*256*256*256 different IP addresses = 4.3 Billion!
Is that enough?
Do we still need to remember the 4 numbers?

## Slide 29: Internet Protocol
There aren’t enough unique addresses!
  Various clever ways have been developed to get around this…
    Static vs Dynamic IP
    NAT – hiding many IP addresses behind one
    IPv6 – The latest version of IP
I can’t remember my IP address!
  The DNS means we don’t need to…
    Domain Name Server / Service (DNS)
    A further translation of the IP address into Natural Language
      BELTA or KCOSH or Kitchen PC or www.bbc.co.uk

## Slide 30: Twisted Pair Wire
+ Thin & Flexible cable
+ Cheaper than other cables

## Slide 31: Coaxial Cable
Commonly used for Video links
Semi conductor surrounds copper wire to protect signal strength

## Slide 32: Fibre Optics
Uses medium of light
Very fast
Flexible, but comparatively expensive

## Slide 33: Network Topology 1
Centralised Network
  Close control
  Inefficient
  Single point of failure
  Limited by central node capacity

## Slide 34: Network Topology 2
Decentralised Network
  Greater Admin Burden
  Weakened Control
  Greater Efficiency
  Robust

## Slide 35: Network Topology 3
Distributed Network (P2P)
  Shortest Route Efficiency
  Multiple Route Efficiency
  Infinitely Scalable
  Robust
  Congestion
    Backbone capacity
  Admin Difficulties
    Standards and Policies

## Slide 36: Increasing Network Bandwidth
Reliance on the backbone – the red lines.
Focus on Improving the speed, capacity and quality of network backbone
  For example;
    Trans Atlantic, connecting Europe with US.

## Slide 37: Wireless Connection?
Still a need for Fibre optics
  Wireless connection connects to another machine which is part of the network.
  WIFI, Bluetooth
    Use Radio transmission to connect to an antennae – like a walkie talkie!
    The antennae connects through a router to the network
  IrDA
    Uses infra red to transmit between equipment
  The receiver then connects to the rest of the internet.

## Slide 38: Routing
Router
  Chooses the best route through the network for each data stream to take.
  Different packets can take different routes.
We can use Tracert to find out which route we are taking

## Slide 39: Caching
Caching developed to speed information transfer.
  If I want to download the football scores from BBC website.
  Maybe so does my friend John etc.
  Rather than us all connecting to BBC, via US, once I’ve downloaded the information, we can share it.
  It is stored in a cache

## Slide 40: The Future?
oFaster cables
oMore connections
oMore interfaces / devices
oCheaper connections
oBetter reliability

## Slide 41: The Internet
Web 1.0
The Information Web
Web 2.0
The Social Web
Web 3.0
The Intelligent Web

## Slide 42: Web 1.0 View

## Slide 43: Web 2.0 View

## Slide 44: The nature of information changed
Information R/Evolution
Mwesch
http://www.youtube.com/watch?v=-4CV05HyAbM

## Slide 45: Characteristics of Information OR Assumptions about Information
*It is a thing
*It has a logical place
*Where it can be found
On a Shelf
In a File System
In a Category
*Managing Information is Managing Categories
*It Requires Experts
*And is still hard to find.
! ! ! Digital Information is Different ! ! !

## Slide 46: It's an Information Revolution
The responsibility to
Harness
Create
Critique
Organise
Understand
is on Us
Is the world ready?

## Slide 47: Information is Changing
The Machine is Us/ing Us
Mwesch
http://www.youtube.com/watch?v=NLlGopyXT_g

## Slide 48: How did it happen?
XML Separates Form from Content
With Form separated from Content, users did not need to know complicated code to upload content to the web.
We need to rethink a few things...
copyright governance
authorship privacy
identity commerce
ethics love
aesthetics family
rhetorics ourselves
How about in Web 3.0?

## Slide 49: Assignment #1
How has Web 2.0, and how is Web 3.0 affecting the way we think about copyright, governance, authorship, privacy, identity, commerce, ethics, love, aesthetics, family, rhetorics, ourselves?
Group A: Group B:
Group C:
RACHATAYOT WANGSAMER
RAPHEEPHAT AEIPHINGCHAI
PUNN LAOWATCHARA
NATANON SOMBOON
PIYACHAT KAMKLAT
JITTIPAT KAEWIJIT
PAKAWAT SANGCHANTRA
PHUTAWAN MUEANGMA
NOP SUSRI
NATTAPON SUKKEAW
TUNSIRIVUT THOSSAROST
THINNAPOP SRISOMBOON
RANTICHA CHUMJAI
KAUNG KHANT KYAW
HTOO EAIN Y

## Slide 50: Assignment #1
Group D Group E
Group F Group G
Group H Group I
Group J
THANT THUTA NAING
YANG YAOJIE
AUNG KAUNG KHANT
WARINTORN LADLOM
ONG-ARCH SUPARATSAMEE
YIXUAN PAN
PIMCHANOK PANYAPING
DU JIAHAO
PANISARA JANKASEM
CLIVE HUMPHREY NTAMBI
SAW AW MOO DAY CHAN
PATTARAKORN KAEWSAI
KOONTHAWEE KHUEANKAEW
MAY THU KYWEL
HKUN DU
ZUNG MYAW
LI JIAHONG
ATIKAN JAI - ON
CHAWISA PIENRAKKARN
PUTTHAKUN PINGMUEANG
TEETAWAT SAENYEE
NATTAWAT PETCHARAK
ANDAMAN NIWORRANUSIT
MAREEN JAITHAM
KANOK SUKSOMPHONG
JA SENG MAI | 
NYAN THIT SOE | 
PUVIS | BOONPRAMOOK
PEERANAT | KAEOCHINGDUANG
PUNNAVIT | LUANGSUPHA
WIRA LINN | 
PONGBORDIN | NGARMPRASIT
PHONGPANOT | KLEEBBAI
KYI HSOUNG HAY THI |